A reliable protocol on an unreliable channel.
A very rough approach.

---
Connection or not Connection?
Intrinsically in circuit switching architecture
- TCP/IP Levels 0-3
- We may demux packets just by <IPS,IPD,PortS,PortD>
Is it just a heritage of good old TLC guys?
Why don't we do a PnP oriented system?

---
Like circuit switching
- Server needs to allocate hardware resources for each client.
- It -most of all- wants to free the resources once client leaves.
- Freeing up resources and then reloading it up costs very much!
- It wants to know when he leaves!(Teardown)
- So if TCP weren't Connection-oriented we should add the connection in the Application layer!

---
A rough 2-way handshake connection on UDP
Connection waiting (server)
loop {
if ((recvfrom(sockfd, buff, len, 0, from, fromlen)) < 0{exit(EXIT_FAILURE);}
if (*((unsigned char *)buff) == (unsigned char)255) {
if (connect(sockfd, from, *fromlen) < 0) {exit(EXIT_FAILURE);}
int bytes;
while((bytes = writen(sockfd,buff,sizeof(unsigned char)))<=0 ){if(bytes<0){exit(EXIT_FAILURE);}}
break;
}
}
Connection request (client)
unsigned char sendline[1];
sendline[0]=(unsigned char)255;
if ((writen(sockd, sendline, 1)) < 0) {exit(EXIT_FAILURE);}
int letti=0;
sendline[0]=0;
fd_set set;
struct timeval timeout,time;
int rv;
FD_ZERO(&set); /* clear the set */
FD_SET(sockd, &set); /* add our file descriptor to the set */
timeout.tv_sec = TIME_OUT;
timeout.tv_usec = 0;
if(gettimeofday(&time,NULL)!=0){exit(EXIT_FAILURE);}
while(sendline[0]!=(unsigned char)255){
printf("attendo risposta del server\n");
rv = select(sockd + 1, &set, NULL, NULL, &timeout);
if(rv == -1){exit(EXIT_FAILURE);}
else if(rv == 0){return EXIT_FAILURE;}
struct timeval timenow;
if(gettimeofday(&timenow,NULL)!=0){exit(EXIT_FAILURE);}
       if ((timenow.tv_sec - time.tv_sec) >TIME_OUT) {return EXIT_FAILURE;}
letti=readn(sockd, sendline, 1);
   if (letti< 0) {exit(EXIT_FAILURE);}
}
return EXIT_SUCCESS;
- Wait for anything
- Check the magic number
- Connect (important, it will remember IP and port destination and will filter any packet that doesn't come from the client)
- Send the handshake.
- Connection done. (Did server receive my handshake?)
- Send the magic number
- Select with such parameters will wait until socket's buffer isn't empty or time has expired. So to speak we are waiting for the handshake.
- I forgot to put connect into the function!
- Connection done.

---
2 or 3 way handshake?
Less is more Failure scenarios
- For simplicity I considered the 2-way, it's enough for the testing use. The failure scenarios aren't so frequent.
- I'll code the 3-way when I'll reuse this protocol in other consumer programs.
- In order to overwhelm other TCP connections!

---
Receive function
- Receave it and put it in the swapper
- Consistency check on the segment number (rejection)
- Note that I received that segment
- Send the ack
- If the first segment is received save it and push the window
- Finish, inform the sender that buffer is full
loop{
        for (;;) {if ((letti=noisy_readn(fd, (void*)swapper, PACKETSIZE)) < 0) {perror("errore in readn");exit(1);}else if (letti>0){break;}}
        numberreceivedpacket=swapper[0];
if(numberreceivedpacket>(unsigned char)WINDOW ){exit(EXIT_FAILURE);}
bytes[numberreceivedpacket]=letti;
if(((startwindow>endwindow)&&((numberreceivedpacket<startwindow)&&(numberreceivedpacket>endwindow)))||( (startwindow<endwindow)&&((numberreceivedpacket<startwindow)||(numberreceivedpacket>endwindow)))){continue;}
alreadyreceived[numberreceivedpacket]=(unsigned char)1;
        unsigned char* swap=NULL;
swap=swapper;
        swapper=pacchettiptr[numberreceivedpacket];
        pacchettiptr[numberreceivedpacket]=swap;
        for (;;) {
if ((letti=noisy_writen(fd, (void*)&numberreceivedpacket, sizeof(unsigned char))) < 0) {perror("errore in writen");exit(1);}else if(letti>0)}break;}}
        while(alreadyreceived[startwindow]==(unsigned char)1){
memcpy((void*)(buf+*bytescrittisubuffer),(void*)&pacchettiptr[startwindow][1],bytes[startwindow]-1);
*bytescrittisubuffer = *bytescrittisubuffer+bytes[startwindow]-1;
if(*bytescrittisubuffer==n){
--------------------------------------------------------
}
alreadyreceived[startwindow]=0;
startwindow=(startwindow+1)%WINDOW;
endwindow=(endwindow+1)%WINDOW;
 }
}

---
The swapper
Pointers (pacchettiptr)
Data copy avoidance
swappertofree=swapper;
loop{
        for (;;) {if ((letti=noisy_readn(fd, (void*)swapper, PACKETSIZE)) < 0) {perror("errore in readn");exit(1);}else if (letti>0){break;}}
        numberreceivedpacket=swapper[0];
[..]
        unsigned char* swap=NULL;
swap=swapper;
        swapper=pacchettiptr[numberreceivedpacket];
        pacchettiptr[numberreceivedpacket]=swap;
        [..]
}
[..]
//swappertofree Is needed to remember the address of the “Little Memory” to free it up after all.
[..]
free(swappertofree);
[..]
i
Swapper
Segment(i)
It will go in the memory area pointed by Swapper
Little Memory
Window
Memory

---
The swapper
Pointers (pacchettiptr)
Data copy avoidance
swappertofree=swapper;
loop{
        for (;;) {if ((letti=noisy_readn(fd, (void*)swapper, PACKETSIZE)) < 0) {perror("errore in readn");exit(1);}else if (letti>0){break;}}
        numberreceivedpacket=swapper[0];
[..]
        unsigned char* swap=NULL;
swap=swapper;
        swapper=pacchettiptr[numberreceivedpacket];
        pacchettiptr[numberreceivedpacket]=swap;
        [..]
}
[..]
//swappertofree Is needed to remember the address of the “Little Memory” to free it up after all.
[..]
free(swappertofree);
[..]
j
i
Swapper
Segment(j)
It will go in the memory area pointed by Swapper
Little Memory
Window
Memory

---
The swapper
Pointers (pacchettiptr)
Data copy avoidance
swappertofree=swapper;
loop{
        for (;;) {if ((letti=noisy_readn(fd, (void*)swapper, PACKETSIZE)) < 0) {perror("errore in readn");exit(1);}else if (letti>0){break;}}
        numberreceivedpacket=swapper[0];
[..]
        unsigned char* swap=NULL;
swap=swapper;
        swapper=pacchettiptr[numberreceivedpacket];
        pacchettiptr[numberreceivedpacket]=swap;
        [..]
}
[..]
//swappertofree Is needed to remember the address of the “Little Memory” to free it up after all.
[..]
free(swappertofree);
[..]
j
i
Swapper
And so on
Little Memory
Window
Memory

---
Send function (1)
- If there are some segments in the window, which have been never sent, send it
- Calculation of segment size
- Send the segment
- Refresh the written bytes
- Add the segment information -clock included- to check and resend it when it'll expire
- Check if it was the last segment of the window or go forward
loop{
if ((finestrafinita == 0)&&(n-*scritto>0)) {
buffer[0] = (unsigned char)ptr;
if (n - *scritto >= PACKETSIZE) {
byte_inf[ptr] = *scritto;
byte_scritti[ptr] = PACKETSIZE - 1;
dim = PACKETSIZE-1;
} else if (n - *scritto < PACKETSIZE) {
byte_inf[ptr] = *scritto;
dim = n - *scritto;
byte_scritti[ptr] = n - *scritto;
}
memcpy(buffer + 1, buf + *scritto, dim);
for (;;) {
if ((bytes = noisy_writen(fd, buffer, dim+1)) < 0) {exit(1);}else if (bytes == dim+1)break;}
*scritto = *scritto + dim;
if(gettimeofday(&times[ptr],NULL)!=0){exit(EXIT_FAILURE);}
ptrarr[ptr]=(unsigned char)ptr;
list_put(&lista,(void*) &times[ptr], &ptrarr[ptr], ptr);
if (ptr == ptrsup)
finestrafinita = 1;
else {
ptrinc(&ptr);
}
}
[...]

---
Send function (2)
- Preparation for the select timeout
- Read acks, timeout is needed to avoid loop when we are only waiting for acks.
- Received ack of the oldest segment, go forward
- Other segment's ack received: remove it from the list and refresh timeout with the estimated RTT
- If we sent all of the bytes and the list of not-acked segments is empty, close and do 2-way handshake
int rv;
FD_ZERO(&set); /* clear the set */
FD_SET(fd, &set); /* add our file descriptor to the set */
timeout.tv_sec = 0;
timeout.tv_usec = 500;
for(;;){
rv = select(fd + 1, &set, NULL, NULL, &timeout);
if(rv == -1){exit(EXIT_FAILURE);}
else if(rv == 0){break;}
letti=noisy_readn(fd, buffer, PACKETSIZE);
   if (letti< 0) {exit(EXIT_FAILURE);}
ptrletto = (unsigned char)buffer[0];
if(ptrletto==(unsigned char)254){
[chiudo e handshake]
}
if(checklist(&lista,ptrletto)==0){
continue;
}
RECV:
if (ptrletto == ptrinf) {
unsigned char i=ptrletto;
do {
ptrinc(&ptrinf);
ptrinc(&ptrsup);
ack[i]=0;
i+=(unsigned char)1;
i%=WINDOW;
if(finestrafinita==1){
ptrinc(&ptr);
finestrafinita =0;
}
}while( (i!=ptrsup) && (ack[i]==1));
}
else
ack[ptrletto]=(unsigned char)1;
if(gettimeofday(&nowtime,NULL)!=0){exit(EXIT_FAILURE);}
if(resendlimiter[ptrletto]!=0){
if(list_empty(&lista)==0){
if(nowtime.tv_sec>times[ptrletto].tv_sec){time_out=(time_out/4)*3 +(((nowtime.tv_sec- times[ptrletto].tv_sec)/4)*1000000) + (nowtime.tv_usec - times[ptrletto].tv_usec)/4;}
}
list_remove(&lista, ptrletto);
}
else{
time_out=TIME_OUT*1000000;
}
resendlimiter[ptrletto]=5;
        }
if((n-*scritto<=0)&&(list_empty(&lista)==1)){
[two way handshake e fine trasmissione]
}

---
Too much simple timeout
Very high!
- When ack has been received: timeout=oldtimeout*3/4 + timetoack/4
- When a timeout has occurred: timeout=oldtimeout/2 + defaulttimeout/2
- When a desynch occurs: timeout=defaulttimeout
Next slide
- It doesn't work very well.
- A too small timeout is often fails!
- Better consider the standard deviation like TCP already does.

---
Resend limiter (desynch issue)
Window size 3
Unacked and unackable, deadlock
sender
receiver
0
7
7
1
0
0
2
6
1
1
6
exp 0
sender
receiver
exp 0
2
5
2
exp 0
5
4
4
3
3
- After 5 unacked resend, sender will try to go forward even if this segment isn't acked and timeot will be resetted.
- It's just one way to fix it. Sure not the best one.
- Use the byte number like TCP does.

---
Strange List (1)
NextNode pointer
nodes
Array of node's pointer
Generic state
i
i+1
Memory
Window's size

---
Strange List (2)
NextNode pointer
nodes
Array of node's pointer
- i segment's ack received
- Have to remove this segment from the list!
i
i+1
Memory
Window's size

---
Strange List (2)
NextNode pointer
nodes
Array of node's pointer
- Suppose i segment expired instead
- So after removing it like we did in the last slide
- Resend the i segment
- Have to add it to the list!
i
i+1
Memory
Hence
i+2
- The list is alway ordered
- Only needed to check up the first entry timeout!
Window's size

---
Next season: Things I'd like to do
- Make it full duplex
- Variable window size
- Better handling of timeout
- Disconnection function
- 3-way handshake
- Polish the code
- Statistics measurements
- Have fun overwhelming other TCP connections!